## Slide 20
Notes: Charger communication protocols and downfalls found. OCPP 1.6j communicating in a WH indication for both AC and DC.
When you plug a charging connector into a vehicle, two separate digital conversations occur with the charger sitting in between the two. The first conversation is between the vehicle and the charger, where the vehicle asks the charger for power and the charger must understand the request in order to deliver. This conversation tends to be guided either by ISO 15118, which was developed by the International Standardization Organization (ISO), or by DIN SPEC 70121, where DIN stands for the German Institute for Standardization, a non-profit organization serving as the national body for standardization. On the other side, the charger talks to the network operator to authorize payments, track the charging session, provide status updates to the driver’s phone app, and allow the operator to see any problems with the charging session. This communication process is typically guided by a protocol developed by the Open Charge Alliance (OCA) called Open Charge Point Protocol (OCPP).
OCPP 1.6j does not utilize TLS and generally requires no security or is password protected.

## Slide 34
Notes: Things to keep in mind while testing EVSE for type approval.
mobile application must have required markings.

## Slide 35
Notes: Discuss the inability for some chargers to display the totalizer value during the initial type evaluation. Activation methods an issue for some devices in the field, especially if they are only RFID activated. Markings on HMI and receipt must match, agreement of indications. Discuss zero placeholder and power loss not shown on receipt. Some pitfalls I have seen is trying to list a disclaimer for power loss on every receipt. Requirement to display on receipt that the session was ended due to power loss.
ISO 15118 communication errors with tesco, TESCO and TESLA communication errors. Possibly more to come.